## Slide 1
Project Apollo
An open source oxygen concentrator
http://project-apollo.org
Microsoft Volunteers
Carsten Avenhaus, Stephen Carlson, Adi Oltean,
Saqib Shaik, Shivkumar Swaminathan HelpfulEngineering.org non-profit (19K volunteers!)
Devon Rowland Quick2space.org non-profit
Adi Oltean

## Slide 2
Why
  O2 needed for ventilators, oxygen therapy
    Typical FiO2 0.3 … 0.5, up to 1
  Oxygen generation is a big problem in developing countries
    No established infrastructure
    Oxygen bottles are expensive
  People are already looking at alternative (local) ways for producing and delivering oxygen
Project Apollo
https://www.economist.com/graphic-detail/2021/03/09/hospitals-are-running-out-of-oxygen-to-treat-covid-19-patients
https://www.cidrap.umn.edu/news-perspective/2021/03/who-sounds-alarm-over-covid-linked-oxygen-crisis
https://apnews.com/article/oxygen-crisis-africa-latin-america-eb0d2731a8613c1ae218db7d32a227a6

## Slide 3
What is it
  Goal = enabling people around the world to build the prototype ASAP
  Focus = Simplicity and speed of build
    Simple, reliable design (zeolite-based PSA system)
    Flexible, open source, off-the-shelf materials
    Very low cost (aspirational target = $200 for 15 liters/min @ 80%)
  Final goal = Enable people to iterate and publish their own designs in the community
Project Apollo

## Slide 4
Project Apollo v4
Apollo v4
  Focus = medical device
    Safety: detect all failure scenarios
    Ease of use: User experience and maintainability. Clear, actionable error messages
    Self-regulating: Patient sensor/data feedback loop
  Control box
    Touch screen for diagnostic messages, medical-grade buzzer
    Open source, modular PCB design. Works with a variety of sensors
    Self-tuning: valve timing, auto-adjusts to changes in compressed air input pressure, machine learning
    Integration with SpO2 oximeter Bluetooth sensor
    Cloud data integration for patient monitoring
  Self-contained enclosure
    Built-in compressor
    Full focus on thermals, airflow, noise reduction
Collaborations
  Funding: Quick2space.org
  Volunteers: Helpful Engineering, Microsoft Garage, Public Invention
Documentation, code
  http://project-apollo.org

## Slide 5
Apollo - Hack4Good Spring 2021
http://project-apollo.org
What we have achieved in this hackathon
  PCB schematic/layout for the valve board
    What is it: central PCB to drive all valves and detect failures
    What we did: finalized Friday late night!
  Prototyped integration of SpO2 oximeter sensor into Apollo code
    What is it: Allows reading of SpO2 oxygen concentration in blood
      Used this as a closed feedback loop to drive oxygen output
      Important to not deliver too much oxygen!
    What we did: prototyped and integrated Bluetooth LE code
  Project Bonsai ML simulator code
    What is it: Uses Reinforcement Learning to self-optimize the concentrator
    What we did: Repro previous results in a separate Azure Bonsai instance, Document simulation code
  Apollo v4 software
    What is it: the “brain” behind the oxygen concentrator
    What we did: Code cleanup, adding comments

## Slide 6
Apollo v4: Bluetooth SpO2 sensor
http://project-apollo.org

## Slide 7
Apollo v4: valve board schematic
http://project-apollo.org

## Slide 8
Apollo v4: valve board layout
http://project-apollo.org

## Slide 9
Conclusion
http://project-apollo.org
Key items developed/prototyped
  Valve board, SpO2 sensor, Apollo software, Apollo ML simulator stack
Next steps
  Finalize Apollo v4 in the next 3-6 months
  FDA emergency use approval
Thanks
  Microsoft Hack4good community
    for helping create the context for amazing work
  Helpful Engineering.org non-profit
    Community of 19,000 engineers going strong
    Help from QA/RA volunteers from the medical industry helping with regulatory compliance
    Help with FDA certification of the upcoming device
  Quick2space.org
    support/funding for materials

## Slide 10
Thank you!
http://project-apollo.org

## Slide 11
Published one year ago
  Oxygen concentrator prototype using household materials
  Build instructions - documentation
  $260 material cost – BOM
Multiple iterations/variants have been built
  O2 concentration 45 … 70%, 5 lpm
Project Apollo v2 (previous work)

## Slide 12
Apollo v4 (previous work)
http://project-apollo.org