## Slide 1
Why
  O2 needed for ventilators, oxygen therapy
    Typical FiO2 0.3 … 0.5, up to 1
  Oxygen generation is a big problem in developing countries
    No established infrastructure
    Oxygen bottles are expensive
  People are already looking at alternative (local) ways for producing and delivering oxygen
Project Apollo
https://www.economist.com/graphic-detail/2021/03/09/hospitals-are-running-out-of-oxygen-to-treat-covid-19-patients
https://www.cidrap.umn.edu/news-perspective/2021/03/who-sounds-alarm-over-covid-linked-oxygen-crisis
https://apnews.com/article/oxygen-crisis-africa-latin-america-eb0d2731a8613c1ae218db7d32a227a6

## Slide 2
What is it
  Goal = enabling people around the world to build the prototype ASAP
  Focus = Simplicity and speed of build
    Simple, reliable design (zeolite-based PSA system)
    Flexible, open source, off-the-shelf materials
    Very low cost (aspirational target = $200 for 15 liters/min @ 80%)
  Final goal = Enable people to iterate and publish their own designs in the community
Project Apollo

## Slide 3
Project Apollo v4
Apollo v4
  Focus = medical device
    Safety: detect all failure scenarios
    Ease of use: User experience and maintainability. Clear, actionable error messages
    Self-regulating: Patient sensor/data feedback loop
  Control box
    Touch screen for diagnostic messages, medical-grade buzzer
    Open source, modular PCB design. Works with a variety of sensors
    Self-tuning: valve timing, auto-adjusts to changes in compressed air input pressure, machine learning
    Integration with SpO2 oximeter Bluetooth sensor
    Cloud data integration for patient monitoring
  Self-contained enclosure
    Built-in compressor
    Multi-stage moisture removal
    Full focus on thermals, airflow, noise reduction
Collaborations
  Funding: Quick2space.org
  Volunteers: Helpful Engineering, Microsoft Garage, Public Invention
Documentation, code
  http://project-apollo.org

## Slide 4: Project Apollo – conclusions
Description
O2 Concentrator: Simple, reliable design (zeolite-based PSA system). Flexible, open source, using off-the-shelf materials
Differentiators
Very low cost (aspirational target = $250 for 15 liters/min @ 90%) – current BOM cost range on prototypes have been $260-450 with retail ordered parts and components (not including cost of compressor and oxygen sensor) Safety & Usability: Detect all failure scenarios, User experience and maintainability. Clear, actionable error messages, Alarm sensors Self-regulating: Patient sensor/data feedback loop Touch screen for diagnostic messages, medical-grade buzzer, large 2.8" LED screen, localizable messages in any locale/character set Open source, modular PCB design. Works with a variety of sensors Self-tuning: valve timing, timing adapts in changes in temperature, variations in physical dimensions, zeolite age, auto-adjusts to changes in compressed air input pressure, machine learning. Integration with SpO2 oximeter Bluetooth sensor Cloud data integration for patient monitoring Built-in compressor, self contained enclosure – humidity and filtering, optimized airflow, thermals/cooling and noise reduction
Target: Product Quality Standards and Prototype Readiness
Compatible and adaptable with the Indian Supply Chain driven BOM Compliant with new Indian Govt. guidelines on O2 Concentrator Feature sets Can be assembled in a lead time of 4-5 hours given availability of parts

## Slide 5: Project Apollo Partners, collaborators
Microsoft Garage